## Slide 1: Chapter 2: Configure a Network Operating System
Introduction to Networks v5.1

## Slide 2: Chapter Outline
2.0 Introduction
2.1 IOS Bootcamp
2.2 Basic Device Configuration
2.3 Address Schemes
2.4 Summary

## Slide 3: Section 2.1: IOS Bootcamp
Upon completion of this section, you should be able to:
Explain the purpose of Cisco IOS.
Explain how to access a Cisco IOS device for configuration purposes.
Explain how to navigate Cisco IOS to configure network devices.
Describe the command structure of Cisco IOS software.

## Slide 4: Topic 2.1.1: Cisco IOS

## Slide 5: Operating Systems
Notes: 2.1.1.1 Operating Systems

## Slide 6: Purpose of OS
PC operating systems enable a user to:
  Use a mouse to make selections and run programs.
  Enter text and text-based commands.
  View output on a monitor.
Cisco IOS enables a network technician to:
  Use a keyboard to run CLI-based network programs.
  Use a keyboard to enter text and text-based commands.
  View output on a monitor.
All networking devices come with a default IOS.
It is possible to upgrade the IOS version or feature set.
Notes: 2.1.1.2 Purpose of OS

## Slide 7: Topic 2.1.2: Cisco IOS Access

## Slide 8: Access Methods
Notes: 2.1.2.1 Access Methods

## Slide 9: Terminal Emulation Programs
PuTTY
Notes: 2.1.2.2 Terminal Emulation Programs

## Slide 10: Terminal Emulation Programs (cont.)
Tera Term
Notes: 2.1.2.2 Terminal Emulation Programs (Cont.)

## Slide 11: Terminal Emulation Programs (cont.)
SecureCRT
Notes: 2.1.2.2 Terminal Emulation Programs (Cont.)
2.1.2.3 Activity – Accessing Devices

## Slide 12: Topic 2.1.3: Navigate the IOS

## Slide 13: Cisco IOS Modes of Operation
A console connection must be established before initial configuration of a Cisco device.
After being consoled in, the network technician will have to navigate through various command modes of the IOS CLI.
The Cisco IOS modes use a hierarchical structure and are quite similar for both switches and routers.
Video Available
Notes: 2.1.3.1 Cisco IOS Modes of Operation

## Slide 14: Primary Command Modes
Notes: 2.1.3.2 Primary Command Modes

## Slide 15: Configuration Command Modes
Global Configuration Mode
To configure the device must enter this mode with configure terminal command
Example: Switch(config)#
CLI configuration changes are made that affect the operation of the device as a whole
From this mode, the user can enter different sub-configuration modes
Two common sub-configuration modes include:
Line Configuration Mode - Used to configure console, SSH, Telnet, or AUX access. Example: Switch(config-line)#
Interface Configuration Mode - Used to configure a switch port or router network interface. Example: Switch(config-if)#
Video Available
Notes: 2.1.3.3 Configuration Command Modes

## Slide 16: Navigate Between IOS Modes
Notes: 2.1.3.4 Navigate Between IOS Modes

## Slide 17: Navigate Between IOS Modes (cont.)
Exit
End or Ctrl+Z
Video Available
Notes: 2.1.3.4 Navigate Between IOS Modes

## Slide 18: Topic 2.1.4: The Command Structure

## Slide 19: Basic IOS Command Structure
Notes: 2.1.4.1 Basic IOS Command Structure

## Slide 20: IOS Command Syntax
Notes: 2.1.4.2 IOS Command Syntax

## Slide 21: IOS Help Features
Video Available
Notes: 2.1.4.3 IOS Help Features

## Slide 22: IOS Help Features (cont.)
Video Available
Notes: 2.1.4.3 IOS Help Features

## Slide 23: Hotkeys and Shortcuts
Tab – Completes the remainder of a partially typed command or keyword
Ctrl-R – Redisplays a line
Ctrl-A – Moves cursor to the beginning of the line
Ctrl-Z – Exits configuration mode and returns to user EXEC
Down Arrow – Allows the user to scroll forward through former commands
Up Arrow – Allows the user to scroll backward through former commands
Ctrl-Shift-6 – Allows the user to interrupt an IOS process such as ping or traceroute.
Ctrl-C – Aborts the current command and exits the configuration mode
Notes: 2.1.4.4 Hotkeys and Shortcuts
2.1.4.5 Video Demonstration – Hotkeys and Shortcuts
2.1.4.6 Packet Tracer – Navigating the IOS
2.1.4.7 Lab – Establishing a Console Session with Tera Term

## Slide 24: Section 2.2: Basic Device Configuration
Upon completion of this section, you should be able to:
Configure hostnames on a Cisco IOS device using the CLI.
Use Cisco IOS commands to limit access to device configurations.
Use IOS commands to save the running configuration.

## Slide 25: Topic 2.2.1: Hostnames

## Slide 26: Device Names
Guidelines to Choose a Hostname
Configuring Device Names
Hostnames allow devices to be identified by network administrators over a network or the Internet.
Notes: 2.2.1.1 Device Names

## Slide 27: Configure Hostnames
Syntax Checker Available
Notes: 2.2.1.2 Configure Hostnames

## Slide 28: Topic 2.2.2: Limit Access to Device Configurations

## Slide 29: Secure Device Access
Notes: 2.2.2.1 Secure Device Access

## Slide 30: Configure Passwords
Privileged EXEC Password Example
User EXEC Password Example
VTY Line Password Example
Notes: 2.2.2.2 Configure Passwords

## Slide 31: Configure Passwords (cont.)
Use the enable secret command, not the older enable password command.
The enable secret command provides greater security because the password is encrypted.
Notes: 2.2.2.2 Configure Passwords

## Slide 32: Configure Passwords (cont.)
Console port must be secured.
  Reduces the chance of unauthorized personnel physically plugging a cable into the device and gaining device access.
VTY lines allow access to a Cisco device via Telnet.
  The number of VTY lines supported varies with the type of device and the IOS version.
Notes: 2.2.2.2 Configure Passwords

## Slide 33: Encrypt Passwords
service password-encryption
Prevents passwords from showing up as plain text when viewing the configuration.
Purpose of this command is to keep unauthorized individuals from viewing passwords in the configuration file.
After this command is applied, removing the encryption service does not reverse the encryption
Notes: 2.2.2.3 Encrypt Passwords

## Slide 34: Banner Messages
These are an important part of the legal process in the event that someone is prosecuted for breaking into a device.
Wording that implies that a login is "welcome" or "invited" is not appropriate.
Often used for legal notification because it is displayed to all connected terminals.
Video Available
Notes: 2.2.2.4 Banner Messages
2.2.2.5 Syntax Checker - Limiting Access to a Switch

## Slide 35: Topic 2.2.3: Save Configurations

## Slide 36: Save the Running Configuration File
Startup configuration –File stored in NVRAM that contains all of the commands that will be used upon startup or reboot. NVRAM does not lose its contents when the device is powered off.
Running configuration – File stored in RAM that reflects the current configuration, modifying affects the operation of a Cisco device immediately. RAM loses all of its content when the device is powered off or restarted.
Notes: 2.2.3.1 Save the Running Configuration File

## Slide 37: Alter the Running Configuration
Restore the device to its previous configuration by removing the changed commands individually.
Copy the startup configuration file to the running configuration with the copy startup-config running-config privileged EXEC mode command.
Reload the device with the reload command from privileged EXEC mode.
Switch# reload
  System configuration has been modified. Save? [yes/no]: n
  Proceed with reload? [confirm]
Video Available
Notes: 2.2.3.2 Video Tutorial: Alter the Running Configuration

## Slide 38: Capture Configuration to a Text File
Using PuTTY to Capture Console Session
Notes: 2.2.3.3 Capture Configuration to a Text File

## Slide 39: Capture Configuration to a Text File (cont.)
All session output will be captured to the file specified, MySwitchLogs.
Execute the show running-config or show startup-config command at the privileged EXEC prompt. Text displayed in the terminal window will be placed into the chosen file.
Enabling Session Logging in PuTTY
Notes: 2.2.3.3 Capture Configuration to a Text File (Cont.)

## Slide 40: Capture Configuration to a Text File (cont.)
Disabling Session Logging in PuTTY
Notes: 2.2.3.3 Capture Configuration to a Text File (Cont.)
2.2.3.4 Packet Tracer – Configuring initial Switch Settings

## Slide 41: Section 2.3: Address Schemes
Chapter Objectives:
Explain how devices communicate across network media.
Configure a host device with an IP address.
Verify connectivity between two end devices.

## Slide 42: Topic 2.3.1: Ports and Addresses

## Slide 43: IP Addresses
Connecting End Devices
Configuring a Static IP Address on a Host
Notes: 2.3.1.1 IP Addresses

## Slide 44: Interfaces and Ports
Network communications depend on end user device interfaces, networking device interfaces, and the cables that connect them.
Types of network media include twisted-pair copper cables, fiber-optic cables, coaxial cables, or wireless.
Different types of network media have different features and benefits.
Ethernet is the most common local area network (LAN) technology.
Ethernet ports are found on end user devices, switch devices, and other networking devices.
Cisco IOS switches have physical ports for devices to connect to, but they also have one or more switch virtual interfaces (SVIs). No physical hardware on the device is associated with it. It is created in software.
SVI provides a means to remotely manage a switch over a network.
Notes: 2.3.1.2 Interfaces and Ports

## Slide 45: Topic 2.3.2: Configure IP Addressing

## Slide 46: Manual IP Address Configuration for End Devices
Manually Assigning IPv4 Address Information
Ethernet Adapter Properties
Notes: 2.3.2.1 Manual IP Address Configuration for End Devices

## Slide 47: Automatic IP Address Configuration for End Devices
Assigning Dynamic Addresses
Notes: 2.3.2.2 Automatic IP Address Configuration for End Devices

## Slide 48: Automatic IP Address Configuration for End Devices (cont.)
Verifying Windows PC IP Configuration
Notes: 2.3.2.2 Automatic IP Address Configuration for End Devices (Cont.)

## Slide 49: Switch Virtual Interface Configuration
IP address - Together with subnet mask, uniquely identifies end device on internetwork
Subnet mask - Determines which part of a larger network is used by an IP address
interface VLAN 1 - Interface configuration mode
ip address 192.168.10.2 255.255.255.0 - Configures the IP address and subnet mask for the switch
no shutdown - Administratively enables the interface
Switch still needs to have physical ports configured and VTY lines to enable remote management
Video Available
Notes: 2.3.2.3 Switch Virtual Interface Configuration
2.3.2.4 Syntax Checker – Configuring a Switch Virtual Interface
2.3.2.5 Packet Tracer – Implementing Basic Connectivity

## Slide 50: Topic 2.3.3: Verifying Connectivity

## Slide 51: Interface Addressing Verification
Video Available
Notes: 2.3.3.1 Interface Addressing

## Slide 52: End-to-End Connectivity Test
Video Available
Notes: 2.3.3.2 End-to-End Connectivity Test
2.3.3.3 Lab – Building a Simple Network
2.3.3.4 Lab – Configuring a Switch Management Address

## Slide 53: Section 2.4: Summary
Chapter Objectives:
Explain the features and functions of Cisco IOS Software.
Configure initial settings on a network device using the Cisco IOS software.
Given an IP addressing scheme, configure IP address parameters on end devices to provide end-to-end connectivity in a small to medium-sized business network.
Notes: 2.4.1.1 Class Activity - Tutor Me
2.4.1.2 Packet Tracer - Skills Integration Challenge
2.4.1.3 Chapter 2: Configure a Network Operating System

## Slide 54: Topic 2.4.1: Conclusion